# OBD Mode 11
CyberNet edited this page · 1 revision

Mode 11 - Reset Learn Tables
PID value doesn't matter.
ECU Dump (Mode 22) data is not reset by this operation.
From the memory ranges that are overwritten with default values, it seems related to Fuel, Ignition, TPS calibration.
Could be it does something with DTC storage areas as well.
Request				Reply
Mode	PID		Description	0	1	2	3	4	5	6	7	Parser
0x11	0x0-0xFF		Reset Learn Tables	0x51					only OBD ack (0x11-0x40) is sent back

For pre 08 T4e's just send a Mode 0x11 request (without a PID)
# OBD Mode 22
CyberNet edited this page · 1 revision

Mode 22 - Enhanced Data
PID is 16bit, and the first one starts with a offset of 0x200, as of firmware A131E002 the maximum supported PID is 0x339 (0x200 offset). This table has been generated for a MY09 Elise S - older T4e's have slight variations - in part this table also works for T6E's (Performance Data Dump)
There are gaps in that PID range that are not implemented.
Request				Reply
Mode	PID_Hi	PID_Lo	Description	0	1	2	3	4	5	6	7	Parser
0x22	0x2	0x3	Idle Air Control Learn Value (AC OFF)	0x62	0x2	0x3	L1	L2	L3	L4		L/10240= g/sec Auto learned for Idle Control
0x22	0x2	0x4	Base Idle Speed related - unknown RPM value	0x62	0x2	0x4	B1					B = 8 Bit value - 0x0 - 0xFF limited RPM = 250000 / (480000 / B + 16) * 60
0x22	0x2	0x5	Final Fuel Injector PWM len ???	0x62	0x2	0x5	I1	I2	I3	I4		I1-I4 = 32 bit value - PWM Time Unclear scaling, needs testing
0x22	0x2	0x9	VVL Hi/Low Cam	0x62	0x2	0x9	C					C = 1 = High Cam, 0 = Low Cam
0x22	0x2	0xA	MAF / Catalyst unknown	0x62	0x2	0xA	M1	M2				M1-M2 = 16bit val Unknown value calculated from a lookup table that takes MAF as input. Used within OBD Catalyst functions.
0x22	0x2	0xB	MAF / Catalyst unknown	0x62	0x2	0xB	M1	M2				M1-M2 = 16bit val Unknown value calculated from a lookup table that takes MAF as input. Used within OBD Catalyst functions.
0x22	0x2	0xC	Gear Number	0x62	0x2	0xC	G					G = calculated gear (rpm/speed) 0-6
0x22	0x2	0xD	Calculated Target Idle Speed	0x62	0x2	0xD	S					S = Speed that ECU tries to hold for Idle RPM = (S*5)+600
0x22	0x2	0x11	Read ECU Type	0x62	0x2	0x11	A1	A2	A3	A4		A1-A4 = "T4E","T6" ASCII Bytes
0x22	0x2	0x13	Fuel Air Commanded Ratio (Target AFR)	0x62	0x2	0x13	A1	A2				A1-A2 / 10 = AFR (14.6 ...) Same as Mode 1 Pid 0x44 but 10 times the precision
0x22	0x2	0x14	Solenoid Driver Output Status	0x62	0x2	0x14	SD					SD = Bitmask for L9822 Solenoid Driver 0x1 = fuel pump relay 0x2 = recirculation pump 0x4 = fan fast relay 2 0x8 = fan slow relay 3 0x10 = ac compressor relay 0x20 = TC led 0x40 = VSV Airbox 0x80 = starter relay
0x22	0x02	0x15	TPMS unknown	0x62	0x2	0x15	TPMS1	TPMS2	TPMS3	TPMS4		TMPS1-TMPS4 = 8 Bit values
0x22	0x02	0x16	TPMS unknown	0x62	0x2	0x16	TPMS	TPMS				TMPS-TMPS = 16 Bit value Affects TMPS LED in Cluster
0x22	0x2	0x18	Knock Cylinder 4	0x68	0x2	0x18	K1	K2				K1-K2= 16 Bit Knock related val
0x22	0x2	0x19	Knock Cylinder 1	0x68	0x2	0x19	K1	K2				K1-K2= 16 Bit Knock related val
0x22	0x2	0x1A	Knock Cylinder 2	0x68	0x2	0x1A	K1	K2				K1-K2= 16 Bit Knock related val
0x22	0x2	0x1B	Knock Cylinder 3	0x68	0x2	0x1B	K1	K2				K1-K2= 16 Bit Knock related val
0x22	0x2	0x1C	Read ECU Info 1/8	0x62	0x2	0x1C	A1	A2	A3	A4		A1-A4= ASCII Bytes - example ("Lotus Elise S - RoW MY10")
0x22	0x2	0x1D	Read ECU Info 2/8	0x62	0x2	0x1D	A1	A2	A3	A4		A1-A4 = ASCII Bytes - example ("Lotus Elise S - RoW MY10")
0x22	0x2	0x1E	Read ECU Info 3/8	0x62	0x2	0x1E	A1	A2	A3	A4		A1-A4 = ASCII Bytes - example ("Lotus Elise S - RoW MY10")
0x22	0x2	0x1F	Read ECU Info 4/8	0x62	0x2	0x1F	A1	A2	A3	A4		A1-A4 = ASCII Bytes - example ("Lotus Elise S - RoW MY10")
0x22	0x2	0x21	Read ECU Info 5/8	0x62	0x2	0x21	A1	A2	A3	A4		A1-A4 = ASCII Bytes - example ("Lotus Elise S - RoW MY10")
0x22	0x2	0x22	Read ECU Info 6/8	0x62	0x2	0x22	A1	A2	A3	A4		A1-A4 = ASCII Bytes - example ("Lotus Elise S - RoW MY10")
0x22	0x2	0x23	Read ECU Info 7/8	0x62	0x2	0x23	A1	A2	A3	A4		A1-A4 = ASCII Bytes - example ("Lotus Elise S - RoW MY10")
0x22	0x2	0x24	Read ECU Info 8/8	0x62	0x2	0x24	A1	A2	A3	A4		A1-A4 = ASCII Bytes - example ("Lotus Elise S - RoW MY10")
0x22	0x2	0x25	Alternate IAT (2ZZ)	0x62	0x2	0x25	T1					T1 = Output of lookup table for IAT sensor T1 * 0.625 - 40 = Deg C (LPF'ed)
0x22	0x2	0x26	Engine Load Number	0x62	0x2	0x26	L1					L1 = Engine Load Number (as used in lookup tables)
0x22	0x2	0x27	Engine Coolant Temp (ECT)	0x62	0x2	0x27	T1					T1 = Output of Engine Temp Lookup table T1 * 0.625 - 40 = Deg C (unfiltered - no LPF!)
0x22	0x2	0x2D	ECU Runtime	0x62	0x2	0x2D	T1	T2				T1-T2 = 16 bit val (in 100ms steps) Time(s)=T/10; (used for various delays)
0x22	0x2	0x31	TimingAdvance / Knock related ?	0x62	0x2	0x31	T4	T1	T2	T3		TX (X=Cylinder) unknown Ignition Timing related value
0x22	0x2	0x32	Idle Error Value - unknown	0x62	0x2	0x32	I1	I2				I1-I2 = 16 Bit Idle Error (RPM ?) Value Only valid if Speed < 5kph or Speed > 5kph and RPM are to high.
0x22	0x2	0x3C	Idle Air Control Learn Value (AC ON)	0x62	0x2	0x3C	L1	L2	L3	L4		L/10240= g/sec Auto learned for Idle Control with AC ON
0x22	0x2	0x3D	WSS Left Rear	0x62	0x2	0x3D	S1	S2				S1-S2 = 16 Bit Wheel Speed Value (kmh*100)
0x22	0x2	0x3E	WSS Right Rear	0x62	0x2	0x3E	S1	S2				S1-S2 = 16 Bit Wheel Speed Value (kmh*100)
0x22	0x2	0x3F	WSS Left Front	0x62	0x2	0x3F	S1	S2				S1-S2 = 16 Bit Wheel Speed Value (kmh*100)
0x22	0x2	0x41	WSS Right Front	0x62	0x2	0x41	S1	S2				S1-S2 = 16 Bit Wheel Speed Value (kmh*100)
0x22	0x2	0x42	TractionControl Slip value	0x62	0x2	0x42	SV					SV = 8 Bit Slip value of Traction Control based on actual WSS measurements
0x22	0x3	0x1	Time at TPS 0-1.5%	0x62	0x3	0x1	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x2	Time at TPS 1.5-15%	0x62	0x3	0x2	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x3	Time at TPS 15-25%	0x62	0x3	0x3	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x4	Time at TPS 25-35%	0x62	0x3	0x4	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x5	Time at TPS 35-50%	0x62	0x3	0x5	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x6	Time at TPS 50-65%	0x62	0x3	0x6	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x7	Time at TPS 65-80%	0x62	0x3	0x7	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x8	Time at TPS 80-100%	0x62	0x3	0x8	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x9	Time at RPM 500-1500 rpm	0x62	0x3	0x9	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0xA	Time at RPM 1500-2500 rpm	0x62	0x3	0xA	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0xB	Time at RPM 2500-3500 rpm	0x62	0x3	0xB	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0xC	Time at RPM 3500-4500 rpm	0x62	0x3	0xC	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0xD	Time at RPM 4500-5500 rpm	0x62	0x3	0xD	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0xE	Time at RPM 5500-6500 rpm	0x62	0x3	0xE	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0xF	Time at RPM 6500-7000 rpm	0x62	0x3	0xF	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x10	Time at RPM 7000+ rpm	0x62	0x3	0x10	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x11	Time at KMH 0-30 km/h	0x62	0x3	0x11	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x12	Time at KMH 30-60 km/h	0x62	0x3	0x12	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x13	Time at KMH 60-90 km/h	0x62	0x3	0x13	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x14	Time at KMH 90-120 km/h	0x62	0x3	0x14	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x15	Time at KMH 120-150 km/h	0x62	0x3	0x15	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x16	Time at KMH 150-180 km/h	0x62	0x3	0x16	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x17	Time at KMH 180-210 km/h	0x62	0x3	0x17	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x18	Time at KMH 210+ km/h	0x62	0x3	0x18	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x1A	Time at Coolant Temp 105-110 Deg C	0x62	0x3	0x1A	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x1B	Time at Coolant Temp 110-115 Deg C	0x62	0x3	0x1B	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x1C	Time at Coolant Temp 115-119 Deg C	0x62	0x3	0x1C	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x1D	Time at Coolant Temp 119+ Deg C	0x62	0x3	0x1D	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x1E	Max Engine Speed #1	0x62	0x3	0x1E	RPM1	RPM2	RPM3	RPM4		RPM = 32Bit value of RPM
0x22	0x3	0x1F	Max Engine Speed #2	0x62	0x3	0x1F	RPM1	RPM2	RPM3	RPM4		RPM = 32Bit value of RPM
0x22	0x3	0x21	Max Engine Speed #3	0x62	0x3	0x21	RPM1	RPM2	RPM3	RPM4		RPM = 32Bit value of RPM
0x22	0x3	0x22	Max Engine Speed #4	0x62	0x3	0x22	RPM1	RPM2	RPM3	RPM4		RPM = 32Bit value of RPM
0x22	0x3	0x23	Max Engine Speed #5	0x62	0x3	0x23	RPM1	RPM2	RPM3	RPM4		RPM = 32Bit value of RPM
0x22	0x3	0x24	Max Coolant Temp #1 (at MAX Engine Speed #1)	0x62	0x3	0x24	TEMP1	TEMP2	TEMP3	TEMP4		(TEMP = 32Bit value) - 14d = Fahrenheit
0x22	0x3	0x25	Engine Run Timer #1 (at MAX Engine Speed #1)	0x62	0x3	0x25	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x26	Max Coolant Temp #2 (at MAX Engine Speed #2)	0x62	0x3	0x26	TEMP1	TEMP2	TEMP3	TEMP4		(TEMP = 32Bit value) - 14d = Fahrenheit
0x22	0x3	0x27	Engine Run Timer #2 (at MAX Engine Speed #2)	0x62	0x3	0x27	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x28	Max Coolant Temp #3 (at MAX Engine Speed #3)	0x62	0x3	0x28	TEMP1	TEMP2	TEMP3	TEMP4		(TEMP = 32Bit value) - 14d = Fahrenheit
0x22	0x3	0x29	Engine Run Timer #3 (at MAX Engine Speed #3)	0x62	0x3	0x29	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x2A	Max Coolant Temp #4 (at MAX Engine Speed #4)	0x62	0x3	0x2A	TEMP1	TEMP2	TEMP3	TEMP4		(TEMP = 32Bit value) - 14d = Fahrenheit
0x22	0x3	0x2B	Engine Run Timer #4 (at MAX Engine Speed #4)	0x62	0x3	0x2B	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x2C	Max Coolant Temp #5 (at MAX Engine Speed #5)	0x62	0x3	0x2C	TEMP1	TEMP2	TEMP3	TEMP4		(TEMP = 32Bit value) - 14d = Fahrenheit
0x22	0x3	0x2E	Engine Run Timer #5 (at MAX Engine Speed #5)	0x62	0x3	0x2E	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x2F	Max Vehicle Speed 1	0x62	0x3	0x2F	KMH1	KMH2				KMH = 16Bit value of km/h
0x22	0x3	0x30	Max Vehicle Speed 2	0x62	0x3	0x30	KMH1	KMH2				KMH = 16Bit value of km/h
0x22	0x3	0x31	Max Vehicle Speed 3	0x62	0x3	0x31	KMH1	KMH2				KMH = 16Bit value of km/h
0x22	0x3	0x32	Max Vehicle Speed 4	0x62	0x3	0x32	KMH1	KMH2				KMH = 16Bit value of km/h
0x22	0x3	0x33	Max Vehicle Speed 5	0x62	0x3	0x33	KMH1	KMH2				KMH = 16Bit value of km/h
0x22	0x3	0x34	Fastest Standing Start 0-100KMH	0x62	0x3	0x34	TIME1	TIME2				TIME = 16Bit value of 1/10th seconds (0xFF = never)
0x22	0x3	0x35	Fastest Standing Start 0-160KMH	0x62	0x3	0x35	TIME1	TIME2				TIME = 16Bit value of 1/10th seconds (0xFF = never)
0x22	0x3	0x36	Last Standing Start 0-100KMH	0x62	0x3	0x36	TIME1	TIME2				TIME = 16Bit value of 1/10th seconds (0x00 = never)
0x22	0x3	0x37	Last Standing Start 0-160KMH	0x62	0x3	0x37	TIME1	TIME2				TIME = 16Bit value of 1/10th seconds (0x00 = never)
0x22	0x3	0x38	Engine Run Timer overall	0x62	0x3	0x38	DTMS1	DTMS2	DTMS3	DTMS4		DTMS = 32Bit value of 1/10th seconds
0x22	0x3	0x39	Total number of Standing Starts	0x62	0x3	0x39	NUM1	NUM2				NUM = 16 Bit counter

# OBD Mode 2F
CyberNet edited this page · 1 revision

Mode 2F - Test functions
PID range: 0x100-0x164 (not all implemented)
All functions tested on a 1ZZ. Be sure to cycle ignition when starting the car afterwards.
And maybe its not a good idea to fill the cylinders with fuel by triggering the Injectors too much ;-)
Request					Reply
Mode	PID	Data	Description	TPU Test State	0	1	2	3	4	5	6	7	Parser
0x2F	0x100		Unknown read memory function		0x7	0x6F	0x1	0x0	0xf0	0x0	0x0	0x1	Databytes 4-7 return values of memory 0x3F8A28, 0x3F9320, 0x3F9321, 0x3F9A29 (unused in code, no x-references ???)
0x2F	0x101	VAL	Injector #2	0x2	0x4	0x6F	0x1	0x1	VAL				VAL = no effect ? Crankshaft needs to stand still Sets TPUB_Ch01_Par01 (OFFSET) to 2500 - and then back to 100. Also does something on the SPI bus - checks Injector circuits ??? Triggers Injector 40x
0x2F	0x102	VAL	Injector #3	0x3	0x4	0x6F	0x1	0x2	VAL				VAL = no effect ? Crankshaft needs to stand still Sets TPUB_Ch01_Par01 (OFFSET) to 2500 - and then back to 100. Also does something on the SPI bus - checks Injector circuits ??? Triggers Injector 40x
0x2F	0x103	VAL	Injector #4	0x4	0x4	0x6F	0x1	0x3	VAL				VAL = no effect ? Crankshaft needs to stand still Sets TPUB_Ch01_Par01 (OFFSET) to 2500 - and then back to 100. Also does something on the SPI bus - checks Injector circuits ??? Triggers Injector 40x
0x2F	0x104	VAL	Injector #1	0x1	0x4	0x6F	0x1	0x4	VAL				VAL = no effect ? Crankshaft needs to stand still Sets TPUB_Ch01_Par01 (OFFSET) to 2500 - and then back to 100. Also does something on the SPI bus - checks Injector circuits ??? Triggers Injector 40x
0x2F	0x120		Unknown read memory function		0x7	0x6F	0x1	0x20	0xCE (A1)	0x0 (A2)	0x0 (A3)	0x1 (A4)	A1-A4 = values of memory bytes 0x3F8A2A, 0x3F9322, 3F9323, 0x3F9A2B
0x2F	0x121	VAL	VVT PWM duty cycle	0x9	0x4	0x6F	0x1	0x21	VAL				VAL = 0x4-0xFF (if 0x0-0x3 is sent 0x4 is set) Crankshaft needs to stand still Changes PWM duty cycle for VVT to TPU_B_Ch07_Par02 = (3334*VAL)/256 for a duration of 20secs
0x2F	0x122	VAL	VVL PWM duty cycle	0xA	0x4	0x6F	0x1	0x22	VAL				VAL = 0x4-0xFF (if 0x0-0x3 is sent 0x4 is set) Crankshaft needs to stand still Changes PWM duty cycle for VVL to TPU_B_Ch09_Par02 = (3334*VAL)/256 for a duration of 20secs
0x2F	0x125	VAL	Set Instrument Cluster RPM to 3500	0xC	0x4	0x6F	0x1	0x25	VAL (unused)				VAL = 0x4-0xFF (if 0x0-0x3 is sent 0x4 is set) Crankshaft needs to stand still Sends 0x400 messages with 3000rpm for a duration of 20secs
0x2F	0x126	VAL	Set Instrument Cluster SPEED to 100	0xB	0x4	0x6F	0x1	0x26	VAL (unused)				VAL = 0x4-0xFF (if 0x0-0x3 is sent 0x4 is set) Crankshaft needs to stand still Sends 0x400 messages with 100 kph for a duration of 20secs
0x2F	0x127	VAL	Trigger EVAP Purge	0xD	0x4	0x6F	0x1	0x27	VAL				VAL = 0x4-0xFF (if 0x0-0x3 is sent 0x4 is set) OBD Mode 1 Pid 0x2E Commanded Evap Purge Byte gets set to VAL for a duration of 20secs Evap Purge solenoid is triggered
0x2F	0x12A	VAL	Change unkn VVT/VVL value	0xE	0x4	0x6F	0x1	0x2A	VAL				VAL = 0x4-0xFF (if 0x0-0x3 is sent 0x4 is set) changes VVT_VVL_M2F_P12A_val to VAL - seems unreferenced in 1ZZ firmware - for a duration of 20secs
0x2F	0x140		Unknown read memory function		0x7	0x6F	0x1	0x40	0xF7 (A1)	0xE0 (A2)	0x0 (A3)	0x1 (A4)	A1-A4 = values of memory bytes 0x3F8A2C, 0x3F8A2D, 3F9324, 0x3F8A2E
0x2F	0x141	VAL	Fuel Pump	0xF	0x4	0x6F	0x1	0x41	VAL				VAL = compared to Mode 8 VAL (1/0 = on/off) if equal unk_3FE182=1, else unk_3FE182=0 Crankshaft needs to stand still Is active for 1,5 secs then gets reset to 0x0 (TPUState_0xF)
0x2F	0x142	VAL	Airbox Flap	0x16	0x4	0x6F	0x1	0x42	VAL				VAL = 0 (clear bit), >0 (set bit) Sets/Clears a bit in an SPI buffer that controls Airbox Flap solenoid Is active for 2 secs
0x2F	0x143	VAL	Enable Pre/Post O2 Heaters	0x15	0x4	0x6F	0x1	0x43	VAL				VAL = 0 (off), >0 (on) Crankshaft needs to stand still Is active for 20 secs
0x2F	0x144	VAL	Recirculation Pump on	0x14	0x4	0x6F	0x1	0x44	VAL				VAL = 0 (off), >0 (on) Crankshaft needs to stand still Is active for 325 secs
0x2F	0x146	VAL	Fan (lowspeed)	0x10	0x4	0x6F	0x1	0x46	VAL				VAL = compared to Mode 8 VAL (1/0 = on/off) if equal unk_3FE182=0x10, else unk_3FE182=0 Crankshaft needs to stand still Is active for 20 secs then gets reset to 0x0 (TPUState_0x10)
0x2F	0x147	VAL	Set Instrument Cluster MIL LED	0x11	0x4	0x6F	0x1	0x47	VAL				VAL > 0 (Condition to set MIL LED) Crankshaft needs to stand still Is active for 20 secs
0x2F	0x148	VAL	Set Instrument Cluster OIL LED	0x17	0x4	0x6F	0x1	0x48	VAL				VAL > 0 (Condition to set OIL LED) Crankshaft needs to stand still Is active for 20 secs
0x2F	0x149	VAL	Unknown PWM	0x18	0x4	0x6F	0x1	0x49	VAL				VAL = 0 (Clear bit in MPWMSM0), >0 (Set bit in MPWMSM0) Crankshaft needs to stand still Is active for 20 secs
0x2F	0x14A	VAL	Fan (medium)	0x12	0x4	0x6F	0x1	0x4A	VAL				VAL = compared to Mode 8 VAL (1/0=on/off) if equal unk_3FE182=0x8, else unk_3FE182=0 Crankshaft needs to stand still Is active for 20 secs then gets reset to 0x0 (TPUState_0x12)
0x2F	0x14B	VAL	Fan (high)	0x13	0x4	0x6F	0x1	0x4B	VAL				VAL = compared to Mode 8 VAL if equal unk_3FE182=0x4, else unk_3FE182=0 Crankshaft needs to stand still Is active for 20 secs then gets reset to 0x0 (TPUState_0x13)
0x2F	0x160		Unknown read memory function		0x7	0x6F	0x1	0x60	0x0 (A1)	0x0 (A2)	0x0 (A3)	0x0 (A4)	A1-A4 = values of memory bytes 0x3F9325, 0x3F9326, 3F9327, 0x3F9328
0x2F	0x161	VAL	Ignition Coil #1/#4	0x5	0x4	0x6F	0x1	0x61	VAL				VAL = not used Crankshaft needs to stand still Triggers TPU_A_Ch01 / Ch04 Sets Param01 of both channels to TimingAdv_Volts_vs_RPM_LU * 10/16 Is active for 10 secs Pulses Ignition Coils
0x2F	0x162	VAL	Ignition Coil #2/#3	0x6	0x4	0x6F	0x1	0x62	VAL				VAL = not used Crankshaft needs to stand still Triggers TPU_A_Ch02 / Ch03 Sets Param01 of both channels to TimingAdv_Volts_vs_RPM_LU * 10/16 Is active for 10 secs Pulses Ignition Coils
0x2F	0x163	VAL	Ignition Coil #?	0x7	0x4	0x6F	0x1	0x63	VAL				VAL = not used Crankshaft needs to stand still Is active for 10 secs Pulses Ignition Coils
0x2F	0x164	VAL	Ignition Coil #?	0x8	0x4	0x6F	0x1	0x64	VAL				VAL = not used Crankshaft needs to stand still Is active for 10 secs Pulses Ignition Coils

Error message
when engine running, or crankshaft stand still is less than 3 secs
Request			Reply
Mode	PID	Description	0	1	2	3	4	5	6	7	Parser
0x2F	PID	Negativ OBD Reply - Error	0x3	0x7F	0x2F	0x22	0x0	0x0	0x0	0x0	Generic error reply